## Slide 1: Atmospheric modeling of the δ13C-CH4 variability at European measurement sites
Guillaume Monteil(1,2), Sander Houweling(2,1), Thomas Röckmann(1)
Marielle Saunois(3), Philippe Bousquet(3)
IMAU, Utrecht, The Netherlands
SRON, Utrecht, The Netherlands
LSCE, Gif-sur-yvette, France

## Slide 2: δ13C-CH4 in the InGOS project
Objectives:
  Investigate the potential of ICOS extension with high frequency δ13C-CH4 measurements.
    How useful δ13C-CH4 really is?
    Are the model and data precise enough?
Tasks:
  Develop demonstration instrument
  TM5 simulations of CH4 and δ13C-CH4 to assess the potential contribution of European sources to the measurements, and the uncertainties

## Slide 3: Why looking at δ13C-CH4?
Good observational constraint on the total CH4 source
Poor constraint on the source distribution

## Slide 4: Why looking at δ13C-CH4?
Patterns of CH4 and d13C-CH4 differ significantly  potentially useful information
Methodology:
  Build a CH4 sources/sinks budget, and attribute their isotopic signatures
  Generate a base simulation
  Perform sensitivity simulations
    No emissions in Europe (evaluate the background)
    Only anthropic or only natural emissions
    Switch off one single source at a time
  Uncertainty estimation
    Intercomparison with LMDz (transport model errors)
    Propagation of uncertainties in source signatures to modelled mixing and isotopic ratios.

## Slide 5: Base CH4 budget
Anthropogenic sources: EDGAR4.2FT
Natural wetland emissions: LPG-WhyMe
Geologic emissions: GLOGOSS database + scaling to 40 TgCH4/year
+ minor sources (termites, wild animals …)

## Slide 6: Base CH4 budget
Anthropogenic sources: EDGAR4.2FT
Natural wetland emissions: LPG-WhyMe
Geologic emissions: GLOGOSS database + scaling to 40 TgCH4/year
+ minor sources (termites, wild animals …)
Can we distinguish the (individual) European CH4 sources from the background?

## Slide 7: d13C source signatures
Well known (±2‰):
  Wetlands
  Biomass burning
  Enteric fermentation/manure
  Oil and Gas
Less well known (±4‰):
  Rice
  Geology
  Termites
  Landfills
  Coal
Poorly known (±6‰):
  Waste water treatment

## Slide 8: Base CH4 budget: source signatures

## Slide 9: TM5 model
6°x4° global resolution, 1°x1° zoom over Europe
Transported tracers: CH4 and 13CH4. d13C-CH4 reconstructed afterwards
Initial condition: 25 years spinup run with emissions and sinks kept constant
Base simulation from 2005 to 2009
Sensitivity runs from January to December 2009

## Slide 10: δ13C-CH4 in the InGOS project
High-frequency observations (1/hour) across Europe
Needed: a map of the InGOS network and an example of measured time-series
Objectives:
  Better constrain the European CH4 budget
  Improve our knowledge of source signatures  applicable to other regions.
Work to be done:
  What precision is needed to provide useful model results?
  Evaluation of the uncertainties
  Overarching goal: determine whether we can learn something from δ13C-CH4 that we couldn’t learn from CH4.

## Slide 11: TM5 model

## Slide 12: TM5 model

## Slide 13: Measurement sites

## Slide 14: Results: base scenario

## Slide 15: Cabauw tower

## Slide 16: Base scenario

## Slide 17: Base scenario

## Slide 18: Source attribution: natural vs. anthropogenic
Contribution from natural sources (wetlands) easier to distinguish in d13C measurements

## Slide 19: Source attribution: anthropogenic sources
Contribution from natural sources (wetlands) easier to distinguish in d13C measurements
Contributions from agriculture (enteric fermentation + manure, mostly) and fossil fuel sources can be distinguished

## Slide 20: Source attribution: anthropogenic sources (winter)
Contribution from natural sources (wetlands) easier to distinguish in d13C measurements
Contributions from agriculture (enteric fermentation + manure, mostly) and fossil fuel sources can be distinguished
The emissions are very smoothed by the grid size

## Slide 21: Source attribution: other locations

## Slide 22: Daytime observations

## Slide 23: To be done
Observed signals vs. source uncertainties
  Uncertainties in source signatures expected to map strongly in the modelled mixing and isotopic ratios
TM5/LMDz comparison  work in progress
Sub-monthly variability of emissions
Comparison with observations
  When the observations are here
  When the meteorology is there (~mid 2015)

## Slide 24: Conclusions
European sources of CH4 should produce detecteable signals in CH4 and d13C-CH4 measurements
These signals can be interpreted if:
  The uncertainty on source signatures is not too large,
  The model resolution is fine enough (especially the resolution of night-time boundary layer)
 In a first time step, these observations may help better characterize methane source signatures, rather than methane sources themselves.