## Slide 1
TOP DOWN EMISSION ESTIMATES OF RADIATIVELY ACTIVE F-GASES VS BOTTOM UP INVENTORIES
F. Graziosi, F. Furlani, U. Giostra, J. Arduini, S. Reimann, M. K. Vollmer, S. O’ Doherty, N. Schmidbauer, A. Stohl, P. Bonasoni and M. Maione
InGOS 2nd Periodic Project Meeting, Firenze 14-16 October 2014

## Slide 2
European emission of F-gases estimated using in situ long-term high frequency observations from 4 European stations and a Bayesian inversion method (Stohl, 2009).
These estimates are relevant for constraining the atmospheric budget of F-gases on a regional scale, and also for improving the accuracy of global emissions quantification.
The comparison with bottom-up inventories revealed non-negligible discrepancies, thus showing the effectiveness of this approach as a verification tool for declared emissions.

## Slide 3
 | GWP 20 y | GWP 100 y | Lifetime (y)
HFC-32 | 2430 | 677 | 5.2
HFC-125 | 6090 | 3170 | 28.2
HFC-134a | 3710 | 1300 | 13.4
HFC-143a | 6940 | 4800 | 47.1
HFC-152a | 506 | 138 | 1.5
HFC-227ea | 5360 | 3350 | 38.9
HFC-236fa | 6940 | 8060 | 242.0
HFC-245fa | 2920 | 858 | 7.7
HFC-365-mfc | 2660 | 804 | 8.7

## Slide 4
Method I: High-frequency observations

## Slide 5
SRR (Source Receptor Relationship) obtained from FLEXPART 20 d backward calculations for 2008.
40.000 particles released every 3 h;
For 2008 2009 we used ECMWF data with 0.25 x 0.25 ° resolution (NEST). For the remaining years we used 1°x1° resolution (NO NEST)
The FLEXPART output is ingested by the inversion algorithm based on the analytical inversion method by Stohl et al. (2009);
An a posteriori emission distribution leading to the best fit between the measurements and the model results is found.
Multiplying the SRR with an emission flux taken by an appropriate a priori emission field gives the simulated mixing ratio at the receptors to be compared with the measurements
We used as a priori HFCs’ emissions reported by EDGAR v 4.2 spatial resolution 0.1 x 0.1°lat long and UNFCCC bottom up estimates
Emissions are then grouped in cells 0.5x0.5° lat long. Emissions intensity and distribution are given
Method II: Bayesian Inversion

## Slide 6: Sensitivity test A
Emissions uncertainty
derived by max err* :
A priori field intensity modulation
Station geometry
*Max err=(max_value –min_value)/2
Edgar x 0.5
Edgar x 1.0
Edgar x 2.0
No ZEP
No JFJ
No MHD
No CMN

## Slide 7
Station geometry
Notes: Basando la stima delle emissioni con una stazione in meno si commettono errori al massimo del ± 20% circa.
Curioso il caso di MHD: quando lo togliamo commettiamo una sovrastima sistematica per ogni composto.
Forse perché (dopo ZEP) è il segnale con meno spikes e quando è presente “pulisce” il dominio. Dovrebbe accadere anche con ZEP, ma forse non ha abbastanza sensitività nel dominio

## Slide 8: Sensitivity test B
Different a priori field
  Edgar Vs UNFCCC
  Different emission intensity
  Different emission distibution
Edgar
UNFCCC
Notes: Inserire tabella con diff percentuali tra i due data set.
Inserire grafici istogramma

## Slide 9
A posteriori emission field comparison
A priori emission field comparison
Notes: Casi più importanti:
HFC-245fa: A priori c’è una differenza di 3 ordini di grandezza, a posteriori c’è un differenza di un solo ordine di grandezza.
HFC-227ea: A priori c’è una differenza di quasi un ordine di grandezza, a posteriori c’è una differenza di meno di un fattore 2 (94%).

## Slide 10: Sensitivity test C
wind field spatial resolution:
  NO NEST1° x 1°
  NEST 0.25° x 0.25°
Notes: Inserire istogramma

## Slide 11: Results

## Slide 12
Notes: Nota: Edgar 4.2 fornisce dati fino al 2008. Noi li abbiamo estrapolati linearmente fino al 2012 per poter fare il confronto. L’estrapolazione è stata fatta basandosi sui dati dal 1998 al 2008.

## Slide 13: Time series of HFC-125 European emission estimates divided by macro-areas

## Slide 15
Notes: Per il 152a L’UNFCCC non ha dati di emissione per l’italia, l’austria, la romania e la slovenia.

## Slide 16
Notes: La stima delle emissioni inizia da quando abbiamo almeno due stazioni.

## Slide 18
Notes: Qui dobbiamo stare attenti: per 227ea e per il 245fa francesco ha iniziato la stima delle emissioni dal 2006 anche se abbiamo JFJ e MHD per i soli ultimi 3 mesi.

## Slide 19
Notes: Secondo edgar viene emesso solo da: Germania, Spagna, Repubblica ceca e Slovacchia
Secondo UNFCCC è emesso anche da Polonia, Lituania, Croazia, Ungheria.

## Slide 20
Notes: UNFCCC ha dati di emissione solo per Repubblica Ceca e Francia.
Secondo Edgar emettono tutti i paesi europei